## Slide 1: Fractional Factorial Design
Full Factorial Disadvantages
  Costly (Degrees of freedom wasted on estimating higher order terms)
Instead extract 2-p fractions of 2k designs (2k-p designs) in which
  2p-1 effects are either constant 1 or -1
  all remaining effects are confounded with 2p-1 other effects
Notes: Some effects are observed at only one level. The last bullet needs further elaboration—be patient

## Slide 2: Fractional Factorial Designs
Within each of the groups, the goal is to
  Have no important effects present in the group of effects held constant
  Have only one (or as few as possible) important effect(s) present in the other groups of confounded effects

## Slide 3: Fractional Factorial Design from a full factorial
Consider a ½ fraction of a 24 design
We can select the 8 rows where ABCD=+1
  Rows 1,4,6,7,10,11,13,16
  Use main effects coefficients as a runs table
This method is unwieldy for a large number of factors

## Slide 4
Run | A | B | C | D | AB | AC | AD | BC | BD | CD | ABC | ABD | ACD | BCD | ABCD
(1) | -1 | -1 | -1 | -1 | 1 | 1 | 1 | 1 | 1 | 1 | -1 | -1 | -1 | -1 | 1
a | 1 | -1 | -1 | -1 | -1 | -1 | -1 | 1 | 1 | 1 | 1 | 1 | 1 | -1 | -1
b | -1 | 1 | -1 | -1 | -1 | 1 | 1 | -1 | -1 | 1 | 1 | 1 | -1 | 1 | -1
ab | 1 | 1 | -1 | -1 | 1 | -1 | -1 | -1 | -1 | 1 | -1 | -1 | 1 | 1 | 1
c | -1 | -1 | 1 | -1 | 1 | -1 | 1 | -1 | 1 | -1 | 1 | -1 | 1 | 1 | -1
ac | 1 | -1 | 1 | -1 | -1 | 1 | -1 | -1 | 1 | -1 | -1 | 1 | -1 | 1 | 1
bc | -1 | 1 | 1 | -1 | -1 | -1 | 1 | 1 | -1 | -1 | -1 | 1 | 1 | -1 | 1
abc | 1 | 1 | 1 | -1 | 1 | 1 | -1 | 1 | -1 | -1 | 1 | -1 | -1 | -1 | -1
d | -1 | -1 | -1 | 1 | 1 | 1 | -1 | 1 | -1 | -1 | -1 | 1 | 1 | 1 | -1
ad | 1 | -1 | -1 | 1 | -1 | -1 | 1 | 1 | -1 | -1 | 1 | -1 | -1 | 1 | 1
bd | -1 | 1 | -1 | 1 | -1 | 1 | -1 | -1 | 1 | -1 | 1 | -1 | 1 | -1 | 1
abd | 1 | 1 | -1 | 1 | 1 | -1 | 1 | -1 | 1 | -1 | -1 | 1 | -1 | -1 | -1
cd | -1 | -1 | 1 | 1 | 1 | -1 | -1 | -1 | -1 | 1 | 1 | 1 | -1 | -1 | 1
acd | 1 | -1 | 1 | 1 | -1 | 1 | 1 | -1 | -1 | 1 | -1 | -1 | 1 | -1 | -1
bcd | -1 | 1 | 1 | 1 | -1 | -1 | -1 | 1 | 1 | 1 | -1 | -1 | -1 | 1 | -1
abcd | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 5: Fractional Factorial Run Matrix
Notes: Write out ABCD and BCD columns of signs. The notation above includes information about both runs and effects.

## Slide 6: Alternate method for generating designs
Alternative method for generating fractional factorial designs
  Assign extra factor to appropriate column of effects table for 23 design
  Use main effects coefficients as a runs table

## Slide 7: Design generator

## Slide 8: Four factors in 8 runs

## Slide 9: Aliased effects
The runs for this design would be (1), ad, bd, ab, cd, ac,bc, abcd
Aliasing
  The A effect would be computed as A=(ad+ab+ac+abcd)/4 – ((1)+bd+cd+bc)/4
  The signs for the BCD effect are the same as the signs for the A effect:
  -,+,-,+,-,+,-,+

## Slide 10: Aliasing
Aliasing
  So the contrast we use to estimate A is actually the contrast for estimating BCD as well, and actually estimates A+BCD
  We say A and BCD are aliased in this situation

## Slide 11: Design Generators
In this example, D=ABC
We use only the high levels of ABCD (i.e., I=ABCD). The factor effects aliased with 1 are called the design generators
The alias structure is A=BCD, B=ACD, C=ABD, D=ABC, AB=CD, AC=BD, AD=BC
The main effects settings for the A, B, C and D columns determines the runs table
Notes: Could use notes on Custom Factorial Designs in Minitab to generate specific designs

## Slide 12: Resolution IV Design
We can apply the same idea to a 26-2 design
  Start with a 24 effects table
  Assign, e.g., E=ABC and F=ABD
  Design generators are I=ABCE=ABDF=CDEF
  This is a Resolution IV design (at least one pair of two-way effects is confounded with each other)

## Slide 13: ¼ Fractional Factorial
For the original 24 design, our runs were (1), a, b, ab, c, ac, bc, abc, d, ad, bd, abd, cd, acd, bcd, abcd
For the 26-2 design, we can use E=ABC and F=ABD to compute the runs as (1), aef, bef, ab, ce, acf, bcf, abce, df, ade, bde, abdf, cdef, acd, bcd, abcdef
Three other 1/4 fractions were available

## Slide 14: Fractional Factorial Analysis
Fractional factorial designs are analyzed in the same way we analyze unreplicated full factorial designs (Minitab Example)
Because of confounding, interpretation may be confusing
E.g., in the 25-2 design, we find A=BD, B=AD, and D=AB significant. What are reasonable explanations for these three effects?
Notes: Minitab analysis

## Slide 15: Screening Designs
Resolution III designs, specifically when 2k-1 factors are studied in 2k runs:
It’s easy to build these designs. For 7 factors in 8 runs, use the 23 effects table and assign D=AB, E=AC, F=BC and G=ABC
Notes: The first Resolution III design is rarely used.

## Slide 16: Screening Design Generators

## Slide 17: Screening Design runs
The design generators are: I=ABD=ACE=BCF=ABCG=11 other terms
The original runs were (1), a, b, ab, c, ac, bc, abc
The new runs are def, afg, beg, abd, cdg, ace, bcf, abcdefg

## Slide 18: Additional topics
Foldover Designs (we can clear up ambiguities from Resolution III designs by adding additional fractions so that the combined design is a Resolution IV design)
Other screening designs (Plackett-Burman)
Supersaturated designs (where the number of factors is approx. twice the number of runs!